## Slide 1: Network Layer
Chapter 4

## Slide 3: Routers & Switches
Part 1
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 4: Types of Networks
Local Area Network (LAN)
  designed for high speed / low latency,
  small-ish area, often a single building or small campus
  typically involving only “customer premises equipment” (CPE)
  Covered in chapter 5
Wide Area Network (WAN)
  designed for long-haul, remote connections,
  typically using lines leased from telephone / comms company
  Interfaces to a LAN at a demarcation point

## Slide 5: Wide Area Network Terms
Customer Premises Equipment – CPE
  What the customer owns, manages, and is responsible for
Channel Service Unit (CSU) / Data Service Unit (DSU)
  Used to connect data terminal equipment (DTE) to a circuit like a T1/T3
  CSU/DSU provides common clock for line cards in a router to sync to telco
Demarc –
  Physical point where provider’s responsibility ends and customer’s begins
Central Office / Switching Office
  Connects customer’s network to providers’ switching network, also PoP
Local Loop –
  Connects demark point to closest central office / switching office

## Slide 6: Forwarding & Routing
Forwarding
  Relaying packets from one network segment to another
  Store & Forward or Cut-Through Switching
Routing
  Uses information encoded in devices address to infer segment to forward to
  Implies existence of rule table to make decision
Bridging
  Makes no inference at all but broadcasts received data to all network segments
  Usually only used for local decisions or to span media

## Slide 7: Why Route?
Three types of segments:
  Shared segment – all hosts share a single wire (10-base2)
  Hub – multiple shares segments connect to a shared hub – still effectively shared
  Switches – switch / store-forward traffic
LAN Congestion – “Collision Domain”
  Too many hosts
  Broadcast storms
  Multicast traffic
  Bandwidth mismatch
Different types of media
Routers are used to break-up broadcast domain, partition networks into different segments, but now we need a way to direct traffic to different segments.

## Slide 8: Routing
Two criteria:
  Ethernet / device IDs – globally unique, but seemingly random assignment
  IP addresses – hierarchical, first bits assigned to a network, last bits assigned to a host
LAN / WAN
  LAN may have routing with L2/L3 switches
  WAN almost always uses L3 routers
Routers vs. Switch?
  Router doesn’t forward broadcast message or multicast
  Routers filter L3 messages, switches don’t
  Switches work on device IDs, try to dynamically build map of devices connected to each port
  Routers work on address, fixed hierarchy of routers

## Slide 9: Forwarding Mechanisms
Source Routing
  Packet includes a selected route determined by sender
  Each router takes strips top instruction and resends, drops packets that don’t match
  Typically used in constrained / local network
  Sources need to know complete path or discover it
  Variable (unbounded?) packet lengths due to lengthy paths

## Slide 10: Forwarding Mechanisms
Virtual Circuits
  Sender establishes a “virtual circuit” through negotiation with intermediate devices
  Sent data always follows that circuit
  Resembles circuit switching but still based on packet switched networks
  More efficient – don’t need to inspect packet contents
  More flexible – allowing different paths for each network flow
  Allows bandwidth reservations
  Finding / reserving a path incurs overhead, not suitable for ad hoc comms

## Slide 11: Forwarding Mechanisms
Table of Global Addresses
  Routers keep a list of next hops
  Packets carry a destination
  Routing decision based on selecting next “best” hop for a given destination
  Routers need to communicate “best routes”
  Source won’t know if a route exists or not
  Global internet addressing means routers need to handle huge #’s of “best routes”

## Slide 12: Network Service Model based on Routing
Network service model describes characteristics of delivery of packets
  Describes what users of a network can expect – not implementation mechanisms
Services may include:
  Guaranteed delivery (or not)
  Bounded delays on delivery time (or not)
  In-order or out-of-order delivery
  Bandwidth guarantees (minimum or maximum)
  Security
Internet’s network service model:
  Best-effort service – packets, bandwidth, and latency aren’t not guaranteed
  Network Neutrality – local provides treat packets equally (or not)

## Slide 13: Routers
Primary functions
  Read packets from input port
  Determine an output port to queue for delivery (or drop)
  Manage the routing tables used to map input to output
Two types:
  Hardware routers – use a hardware accelerated switching fabric
  Software routers – use CPU to make routing decisions
The end of software routers? Software has to forward packets at 51.2ns on a 10gbps link to avoid queueing.
Big impact coming for cloud computing!

## Slide 14: Fast Address Matching
Routers match on address patterns to perform fast lookups
Principle of longest prefix match
Pattern | Interface
1100 1000 0001 0110 1000 0XXX XXXX XXXX | 0
1100 1000 0001 0110 XXXX XXXX XXXX XXXX | 1
1100 1000 0001 XXXX XXXX XXXX XXXX XXXX | 2
XXXX XXXX XXXX XXXX XXXX XXXX XXXX XXXX | 3
Which interface should 1100 1000 0001 0110 1000 0101 1101 0010
forward to?

## Slide 15: Content Addressable Memory
Hardware switching depends on content addressable memory (CAM)
  Cisco calls theirs’ “Ternary Content Addressable Memory”
Formulation of content cells / priority encoding needs to be done during configuration. Software can assist in building these rules.

## Slide 16: Switching Technology
Memory based
  Input data is copied to an output queue on the selected output port
  Example: Catalyst 8500 series routers
Bus based
  Input is transferred directly to output by hardware
  Can be the same “line card” or via shared bus
  Example: Catalyst 9000 series router, 25.6 Tbps aggregate switching capacity
Interconnection Network based
  Dedicated, but software controlled network of parallel busses to allow N simultanoues packets to switch at a time.
  Example: ASR 1000 series, 200Gbps system bandwidth,

## Slide 17: Queueing
Queueing – already discussed
  Network congestion causes queues to fill
  Router delays can add to congestion
  Result the same – dropping packets
Head-of-line blocking occurs when switch fabric is insufficient
  A packet is held due to switch capacity being used by other devices even though there isn’t contention for destination port.
Head-of-line blocking example: The 1st and 3rd input flows are competing to send packets to the same output interface. In this case if the switching fabric decides to transfer the packet from the 3rd input flow, the 1st input flow cannot be processed in the same clock cycle. Note that the 1st input flow is blocking a packet for output interface 3, which is available for processing.
https://en.wikipedia.org/wiki/Head-of-line_blocking

## Slide 18: More Math!
Buffer sizes for adequate performance in queueing routers,
  where is the buffer size (in bits), is the round-trip-time (in seconds), and is the link bandwidth:
  Example: and , then (per port!)
For large numbers of connections, individual flows are likely to be shorter, have similar window sizes, and smaller receive windows, and not constantly sending data:

## Slide 19: Packet Scheduling
Scheduling algorithms:
  Similar, but a little different than process scheduling: no process blocking or starvation
  FIFO – first in, first out
  Priority – attach a priority method to each message, pick highest priority message
  Round-Robin – create queues for each service class, pick from each queue
  Weighted Fair Queueing – packets attached to each per-class queue, then WFQ pulls packets as in RR, but assigns each class a fraction of bandwidth based on weight
One problem similar to OS:
  Buffers may fill with lower-priority traffic leading to priority inversion
Notes: Priority methods: source, destination addresses or ports
Urgency encoded in packet
Service level encoding
Network control messages
Payment agreements (anti-net neutrality)

## Slide 20: Generalized Forward Scheme / Software Defined Network
General forward scheme uses “match + action” rules
There are effectively 11 fields that can be used as matches: Note: inclusion of layer 2 – hardware MAC addresses, and layer 4 TCP/UDP port numbers.
Action: Forward, Drop, Modify-Field
Next generation routing – includes ‘firewall’ with routing decision

## Slide 21: Internet Protocol
Section 2
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 22: Internet Protocol
The Internet Protocol
  Layer 3 of the Internet’s layer cake
IPv4 is “original” – based on 32-bit addressing scheme
  4 billion internet addresses
  Address space is effectively exhausted
IPv6 is “replacement” – based on 128-bit addressing scheme.
  addresses
Notes: Vint Cerf, 1978, later updated to IPv4 in 1983. IPv6 began development in 1998,

## Slide 23: Internet Protocol v4
Four types of network addressing methods:
  Unicast – A one-to-one addressing, sender sends to one receiver
  Broadcast – A one to all addressing scheme, single datagram goes to all endpoints in the broadcast domain.
  Multicast – One to many, or even many to many, datagrams are delivered to a group of recipients in the broadcast domain.
  Anycast – A single destination has multiple routing paths to two or more endpoint destinations, routers will select the best path to one of them (i.e. send this to any one of these)
  Geocast – Delivers to a group of devices in a geographic region.
https://en.wikipedia.org/wiki/Anycast
Underlined means supported by IPv4

## Slide 24: IPv4 Header
Fields of IPv4 Header
  Version – 4 bits
  Header length - 4 bits (where payload begins)
  Type of service – ECN, or other quality fields
  Datagram length – length of IP packet (in bytes)
  ID, Flags, Frag, Offset – Fragment / reordering fields
  TTL – time to live
  Protocol # - 6 – TCP, 17 – UDP1
  Checksum – 1’s complement
  Source & destination addresses
  Options
  Payload
[1] https://en.wikipedia.org/wiki/List_of_IP_protocol_numbers

## Slide 25: IP Datagram Fragmentation
Large IP packets may be fragmented into multiple IP packets
  Layer 2 has an MTU, greater than this and link frames may be fragmented
  Every router on path may use different MTU!
  Packet may be split into multiple fragments (by routers) and reassembled (by routers)
On transmit
  Sender stamps IP w/ a unique ID, source, and destination
Routers
  Split into fragments, create smaller IP datagrams w/ same id, source, and destination
  That means that a payload may not be UDP/TCP, but a fraction of one
  Flag = 1 for all but last fragment, offset sets the location of the fragment
  No retransmit – lost packets are just lost – depends on TCP to rexmit

## Slide 26: IP Addresses
IP Addresses are 32-bit
  Assigned to each host interface (1 to many)
  Represented as: binary, hexadecimal, or “dotted quad” decimals Sloop: 157.160.36.12 / 10011101.10100000.00100100 .00001100 / 9D.A0.24.0C
Addresses must be global unique
  Assigned to organization by IANA in “clumps” called a network address
  Locally, organization can subdivide network into a subnet, or can leave whole
  Organization can route (or not) network
  Internet routes between networks, leaving subnets for local routing
  For example,
    globally, Ship is “157.160.X.X” – we only need one external route for the entire campus
    Internally, Ship is subdivided into multiple subnets: 157.160.36.X is SoE

## Slide 27: Classes Interdomain Routing - CIDR
CIDR is a representation for IP addresses
  Describes the separation between subnet and local host addresses
  Format: a.b.c.d/x – “dotted quad” plus # of bits in network address
  Thus, routers only need to store the CIDR address for each entry:
  Ship is : 157.160.0.0/16, SoE is: 157.160.36.0/22
CIDR makes it “easy” to determine the layout of the host addresses
  Two host addresses are reserved – “.0” is the network #, “.255” is the broadcast, and typically, there is a router address, e.g. “.1”, but that isn’t required, so we say 2 reserved (hint: first / last addresses in subnet are reserved)
CIDR | Hosts | CIDR | Hosts
/30 | 4 – 2 = 2 hosts | /24 | 256 – 2 = 254
/29 | 8 – 2 = 6 hosts | /23 | 512 -2 = 510
/28 | 16 – 2 = 14 hosts | /22 | 1024 – 2 = 1022
/27 | 32 – 2 = 29 hosts | /21 | 2048 – 2 = 2046

## Slide 28: IP Address Assignments
Internet Assigned Number Authority (IANA)
  Sets standards for global IP address allocation and root zone management of DNS
Internet Corporation for Assigned Names and Numbers (ICANN)
  Implements the standards set by IANA
  Maintains central assignment databases
  Assigns addresses to local registrars and maintains “WHOIS” database
Local registrars:
  Assigns domains to assignment blocks
  Assigns numbers to service providers
Service providers:
  Assigns fractions of their IP space to their customers

## Slide 29: IP Addresses – Network Classes
IP version 4 has five “classes” of networks
  Initially used for `classful routing’
Class | Leading Bits | Size Net # | # Nets | Addrs / Net | Start / End
A | 0 | 8 | 128 | 16M | 0.0.0.0 – 127.255.255.255
B | 10 | 16 | 16384 | 64K | 128.0.0.0 – 191.255.255.255
C | 110 | 24 | 2,097,152 | 256 | 192.0.0.0 – 223.255.255.255
D | 1110 | NA | NA | NA | 224.0.0.0 – 239.255.255.255
E | 1111 | NA | NA | NA | 240.0.0.0 – 255.255.255.255
Shippensburg’s IPs start at 157.160, 157 in binary is: 1001 1101, our address starts with the “10” prefix, so we have on of the 16,384 class B networks ever assigned!

## Slide 30: IPv4 Reserved Addresses
CIDR | # of addrs | Description
0.0.0.0/8 | 16M | Current network
10.0.0.0/8 | 16M | Local class A
100.64.0.0/10 | 4M | Shared range for CGN
127.0.0.0/8 | 16M | Loopback addresses
169.254.0.0/16 | 64K | Link local between hosts
172.16.0.0/12 | 1M | Private / Local addrs
192.0.0.0/24 | 256 | IETF Protocol Assignments
192.0.2.0/24 | 256 | TEST-NET-1
192.88.99.0/24 | 256 | IETF Reserved
192.168.0.0/16 | 64K | Private / local addresses
192.18.0.0/15 | 128K | Benchmark subnets
198.51.100.0/24 | 256 | TEST-NET-2
203.0.113.0/24 | 256 | TEST-NET-3
224.0.0.0/4 | 24M | Multicast addresses
240.0.0.0/4 | 24M | Reserved
255.255.255.255/32 | 1 | Broadcast address

## Slide 31: Private Parts
Each routing class defines a range of private network addresses
  These are never routed to the global internet (if they are, they’re dropped)
  They can be used internally to organize a network or create a router backbone
Class | Range | Network Bits | # machines
A | 10.0.0.0/8 | 24 | 16M
B | 172.16.0.0/12 | 20 | 1M
C | 192.168.0.0/16 | 16 | 64K

## Slide 32: IP Address Space Exhaustion
In 2011, IANA assigned its last block of IPv4 Addresses
  Sub-registrars still have some space
  Originally forecast to happen in the early 1990’s
New technologies have accelerated problem
  Multiple addresses per device – your cell phone has wireless, Bluetooth, and cell!
  Small Office / Home Office (SOHO) – 20 – 100 devices per location
New technologies have ameliorated the problem
  NAT / Carrier grade NAT
  IPv6

## Slide 33: Network Address Translation - NAT
NAT is a method of remapping one IP address space into another
  Public facing IP address – an address that is part of the IANA assigned address space
  Private / internal IP address – a non-routable address that is provided by NAT service
  NAT uses a “one to many” approach – one public address maps to many private addresses.
  NAT tracks your outgoing requests and keeps a socket connection established for a flow.
  NAT can also accept incoming requests and forward to a private machine to enable servers in the private network.
  Only one service per IP

## Slide 34: Carrier Grade NAT (CGN)
Carrier Grade NAT
  Used for primarily residential networks, subscribers given a private network address
  The subscriber’s traffic gets routed through ISP’s network and rewritten to face the public internet
  Shifts NAT rewriting from local SOHO to middle-tier on ISP
  Sometimes called NAT444 – connections pass through 3 different IPv4 addressing domains:
    SOHO
    ISP Middle Ware
    Public Internet
  Heavily used in mobile networks – internal routing can migrate through cells
  464XLAT – Locally: IPv4, IPv6 in private network, and then rewritten to IPv4 in public

## Slide 35: Critique of NAT
Breaks the end-to-end principle
  Remember from chapter 2 – application specific features reside only in the end-nodes
  NAT breaks this rule by embedded application specific re-writing in routing nodes
NAT has security, scalability, and reliability issues
  Carrier has to reassemble traffic flow – opens potential for reconstructing data streams
  E.g. ISP could, in theory, inject advertisements into your web pages
Hosting services
  NAT makes it difficult, CGNAT makes it impossible to host services
  Diminishes value to IP address exhaustion problem

## Slide 36: IP version 6
Part 3
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 37: Internet Protocol Version 6
Addresses move to 128-bit
Allows: Unicast, Multicast, and Anycast
Streamlined 40 byte header
Flow labelling
Removes:
  Fragmentation & Reassembly
  Header checksum
  Options
IPv5 was used for experimental Internet Stream Protocol, which predated VOIP & ATM networks

## Slide 38: IPv6 Addresses
128-bit represented as 8 16-bit hex digits – hexatets or quibbles
  Shorthand:
    Leading zeros can be removed from any group: :00fd: = :fd:, :f00d: = :f00d:
    One consecutive section of zeros can be replaced by ::
  Example 1:
    2001:0db8:0000:0000:0000:ff00:0042:8329
    2001:db8:0000:0000:0000:ff00:42:8329 # rule 1, leading zeros
    2001:db8::ff00:42:8329 # rule 2, consecutive zeros
  Example 2:
    2001:0000:0000:00db:0000:0000:0042:0001
    2001:0:0:db:0:0:42:1 # rule 1, leading zeros
    2001::db:42:1 OR 2001:0:0:db::42:1, but NOT: 2001::db::42:1!

## Slide 39: IPv6 Link Local Addresses
All interfaces get a link local address that is valid only for the network segment or issuing broadcast packets (e.g. for configuration discovery)
  IPv6 uses: fe80::/64 (upper 10 bits are fixed, the remaining 64-bits are selected randomly. Initially, the MAC address for the interface, but has since been replaced with a secure hash of the MAC address.

## Slide 40: IPv6 Addressing Additional Features
Hierarchical address assignment
  Formation of super networks
  Allows for route aggregation – e.g. Comcast can be assigned 1 super network, and then the world only needs 1 entry for all of Comcast’s customers
  No need for CIDR
Multicasting addresses built into subnet – no need for special addresses
Stateless Address Autoconfiguration (SLACC)
  fe80::/64 – point to point local link – lower 64-bits pick by local machine
  If no other IPv6 network present, this is sufficient for LAN machines to communicate!

## Slide 41: But wait, there’s more!
Neighbor Discovery Protocol
  Nodes can issue broadcast requests (over their SLACC assigned addresses)
  Allows routes and network prefixes to be shared from neighboring computers
  Alleviates the need for DHCP or other protocols
Internet Protocol Security (IPSec) and Internet Key Exchange (IKE)
  Both are built into IPv6, allowing special header types to be encrypted
Simplified Routing
  Headers are greatly simplified, match modern computer word sizes (128-bit not uncommon), no checksums, no fragments, and no options, thus no optional lengths
Mobility
  Entire subnets can move to new routers without disrupting global routes – move within hierarchy
Jumbograms
  Ipv6 can allow up to 4GB packets, though rarely fully supported today

## Slide 42: An Example
Comcast has been assigned the global IPv6 net: 2601:980::0/32
  That is, the first 32-bits are assigned to Comcast, given them bits of addresses. This is their “super-network.”
  Comcast further subdivided this so that each customer is assigned another 32-bit range (e.g. c100:35). This allows 4 billion customers (more than current IP address!)
  A SOHO subscriber’s router is assigned “2601:980:c100:35::1/64”
  Without using NAT, subscribers can have up to =4 billion machines in their SOHO network.
  Locally, each interface is given a SLAAC address, e.g. 2601:980:c100:35:5130:4cac:402f:fc3e
  Because of dhcp (coming up), each interface is also given an assigned address: 2601:980:c100:35::3eb

## Slide 43: IPv6 Address Classification
Unicast Address – identify single interface
Link local format – non-routable / local subnet only
Multicast – globally routable
Routing Prefix >= 48 bits | Subnet Prefix <= 16bits | Interface 64-bits
Prefix 10-bits | Zeroes 54-bits | Interface 64-bits
Prefix 8-bits | Flag 4-bits | Service Agreement 4-bits | Group ID 112-bits
0 – reserved | 4 – admin local | 8 – org local | 12 – NA
1 – interface local | 5 – site local | 9 – NA | 13 – NA
2 – link local | 6 – NA | 10 – NA | 14 – Global
3 – real local | 7 – NA | 11 – NA | 15 - NA

## Slide 44: IPv6 URL’s
URLs can be complicated, so a new notation was made:
http://[2001:db8:85a3::7348]:443/

## Slide 45: Scoped Link-Local Addresses
Link-local addresses can be scoped to a specific interface:
BSD / OSX use this to identify which interface the address is attached:
fe80:3:……. // interface 3
Also: http://[fe80:3:d939:.....%eth2]/

## Slide 46: IPv6 Special Addresses
Like IPv4, IPv6 has special addresses:
CIDR | # | Use | Purpose
::/0 | 2^128 | Routing | Default route
::/128 | 1 | Software | Unspecified address
::1/128 | 1 | Host | Loopback / Local machine
::FFF:0:0/96 | 2^32 | Software | IPv4 mapped address
::FFFF:0:0:0/96 | 2^32 | Software | IPv4 translated
64:FF9b::/96 | 2^64 | Global inet | IPv4/v6 translated
100::/64 | 2^100 | Routing | Discard
2001::/32 | 2^96 | Global Inet | Terredo Tunnel
2001:20::/28 | 2^96 | Software | ORCHID v2
2001:db8::/32 | 2^112 | Documentation | Example address space
Fe00::/7 | 2^121 | Private network | Unique link local
Fe80::/10 | 2^118 | Private Link | Link-Local
FF00::/8 | 2^120 | Global Internet | Multicast

## Slide 47: Subnets
Part 4
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 48: Subnetting
Subnets
  Reasons for subnetting:
    Balance performance
    Extend the distance of the network
    Isolate problems and reduce odds of catastrophic failure
    Reduce collision domains & broadcast storms
    Partition network into separate independent regions
    Possibly reduce costs
  Costs to subnetting
    Need to join subnets together at L2 or L3
    Additional routing hardware (incurs extra cost !?!)

## Slide 49: Segments using Bridges
Recall bridges
  Connect two or more LAN segments, irrespective of media
  Bridges retransmit data between segments, can do some filtering

## Slide 50: Segments using Switches
Switches work on L2
  Connect multiple LAN segments
  Lead to a “star” topology
  Switch on device addresses
  Can also extend distances
  Pass data simultaneously
  Switches can act as bridges
  Security

## Slide 51: Segments using Routers
Routers work on L3
  Need rules to determine when to forward data
  Media transitions
    Routers don’t just work on ethernet (or compatible)
  Broadcast control
  Packet filtering
  VLAN communications
  Large packet / fragmentation into multiple device frames

## Slide 52: Things to know when creating subnets
Steps to create:
  Determine # of required network IDs
    One for each LAN subnet
    One for each WAN (router) connection
  Determine number of hosts on each subnet
    One for each host / interface
    One for each router interface
    One for broadcast address
    One for network address
  Create subnet mask
    Assign mask for entire network
    Subnet ID for each segment
    Range of host IDs for each segment

## Slide 53: Example – Class C Address
Suppose we have a class C address: 192.168.10.0 / 25
  What is the subnet mask?
  How many subnets?
  How many hosts per subnet?
  What are the valid subnets?
  What are the broadcast and network addresses for each subnet?
  Valid hosts?
Notes: Netmask: 255.255.255.128 / 24 + 1 bit
Subnets: class C has first 24 bits fixed, so we have 1 bit left, so two subnets
How many hosts per subnet? 7 bits for hosts, but we lose two: 2^7-2 = 126
Valid subnets? 192.168.10.0 and 192.168.10.128
Broadcast for each subnet? 192.168.10.127 and 192.168.10.255
Valid hosts: 192.168.10.1 … 192.168.10.126, and 192.168.10.129 .. 192.168.10.254

## Slide 54: Subnet Example
A company has four different “zones” to their network configuration:
Server Zone – publicly facing IP addresses for servers, 7 of them
NAT zone – supports NAT to about 45 users in the various departments, including printers
VPN zone – supports remote workers / VPN & remote desktops (16 connections)
Intranet Zone – internal servers, not public accessibly (hopefully) qty 15.

## Slide 55: Example – Subnet with two hosts
Design a network mask that allows two hosts to communicate point-to-point

## Slide 56: Network Topology, ala Cisco
3-Tier Network for Routing: Core, Distribution, Access
Core
  Switch traffic as fast as possible
  Failure in core results in catastrophic network failure (locally)
  Never slow down traffic, so
    No access lists
    No routing between VLANs
    No packet filtering
    No workgroup access
  Design of core:
    Highly reliable
    Speed & redundancy
    Optimize / rebalance routing tables dynamically

## Slide 57: 3 Layer Routing Topology - Distribution
Distribution
  Workgroup / Aggregation layer
  Provide routing, filtering, and routing to WAN
  Determines how packets enter core
  Distribution layer is where policies are enforced
    Routing
    Access list, filtering, queueing
    Security & network policies
    NAT
    Firewall
    Routing VLAN
    Define broadcast /multicast domains

## Slide 58: 3 Layer Routing Topology - Access
Access Layer
  Controls user and workgroup access to resources
  Network resources users need locally should be here – e.g. local file servers, print servers
  Helps to unload distribution layer

## Slide 59: Collapsed Core (2-tier)
Collapses the core and distribution routers into one unit
  Takes advantage of Moore’s law…
  Main reason: cost savings
  Disadvantages: scalability, size is limited to core capabilities

## Slide 60: Spine-Leaf Topology
Another Cisco topology is the spine-leaf topology
  Uses “Top of Rack” switches in each network chassis
  Servers are redundantly connected to two ToR switches
  Cisco has purpose-built Nexus switches for this purpose
  Spine only connects to other ToR switches
  All ToR switches have same latency
  High bandwidth uplinks handle load-up, prevent slow downs to shared Core

## Slide 61: Basic Troubleshooting - Ping
Ping
  Uses ICMP to send messages to remote IP address
  Ping localhost – if fails, local configuration issue
  Ping local IP address – if fails, network card b0rked
  Ping gateway – if it fails, physical LAN cable or router problem
  Ping remote server – if it fails, problem with WAN connection
  Ping “well known” server like 8.8.8.8 – if it fails, probably a nearby WAN problem

## Slide 62: Basic Troubleshooting – Traceroute
Traceroute
  Uses ICMP messages to passively guess route traffic is following
  UNIX: tracroute, Window: tracert

## Slide 63: Basic Troubleshooting - ARP
ARP – Address Resolution Protocol
  Layer 2 “ethernet” requires the hardware MAC address of receiver
  “arp –a” command lists IPs and hardware MACs – if not found, or mismatch, then there is a layer 2 problem, not a layer 3 problem: